## Slide 1: Integration of Climate Forecasts in Bulk Power System Studies 26-October 2023
Casey Burleyson, Cameron Bracken, and Nathalie Voisin
https://godeeep.pnnl.gov/
PNNL-SA-191582

## Slide 2: Assertions
The existing grid is weather sensitive.
Weather characteristics (e.g., extremes) are changing rapidly.
The grid is also changing rapidly.
A high renewables grid will be even more weather sensitive.

## Slide 3: Key Messages
To assess the resilience and reliability of the bulk power system, it is critical to evaluate system performance:
With coincident load-wind-solar-hydro conditions;
Across a wide range of historical and projected weather conditions.

## Slide 4
Climate &
Social Sciences
Preferred Portfolio
Infrastructure Planning & Siting
Operations Planning & Investment
  Define the portfolio of scenarios that will guide long-term planning
  Analyze resource adequacy under seasonal representative stress events
  Evaluate reliability, economic feasibility, and market incentives for least-cost, resilient operations
Datasets
Climate scenarios, taxes and incentives, market structures, net-zero, technology innovation
10, 20, and 30 year buildouts; wind, solar, load, and hydropower datasets; fuel prices
Electricity prices, technology-specific operations, transmission, storage, key performance
Consistent Integration of Climate Information Throughout the Long-Term Planning Process

## Slide 5: U.S. Climate Projection Dataset
Hot Year
Historic data reproduces observed sequence of past events (1980–2019)
Sequence is repeated twice in the future (2020–2059 and 2060–2099) with additional warming gradually applied
1/8 deg (~12 km) resolution, U.S., hourly
25 hourly and 250+ three-hourly variables
Output is first spatially-averaged by county then population-weighted to create annual 8,760-hr meteorology time series for 54 BAs across the U.S.
Climate data was developed with DOE Sc funding and is publicly available: https://data.msdlive.org/records/cnsy6-0y610

## Slide 6: U.S. Climate Projection Dataset
Hot Year
40 years
Climate data was developed with DOE Sc funding and is publicly available: https://data.msdlive.org/records/cnsy6-0y610
Historic data reproduces observed sequence of past events (1980–2019)
Sequence is repeated twice in the future (2020–2059 and 2060–2099) with additional warming gradually applied
1/8 deg (~12 km) resolution, U.S., hourly
25 hourly and 250+ three-hourly variables
Output is first spatially-averaged by county then population-weighted to create annual 8,760-hr meteorology time series for 54 BAs across the U.S.

## Slide 7: U.S. Climate Projection Dataset
Hot Year
40 years
Climate data was developed with DOE Sc funding and is publicly available: https://data.msdlive.org/records/cnsy6-0y610
Historic data reproduces observed sequence of past events (1980–2019)
Sequence is repeated twice in the future (2020–2059 and 2060–2099) with additional warming gradually applied
1/8 deg (~12 km) resolution, U.S., hourly
25 hourly and 250+ three-hourly variables
Output is first spatially-averaged by county then population-weighted to create annual 8,760-hr meteorology time series for 54 BAs across the U.S.

## Slide 8: Designing Stress Tests Based on Heat Wave Dynamics
Typical heat waves last ~6-7 days and are, on average, symmetric about the maximum temperature day.
~7-day duration

## Slide 9: Designing Stress Tests Based on Heat Wave Dynamics
Heat waves increase peak loads by ~10% on average compared to the background peak loads.
~10% increase
~7-day duration

## Slide 10: Notable Suppression of Wind Generation During Heat Waves
BAs in the Pacific Northwest (e.g., BPAT, PACW, and NWMT) show notable suppression of wind generation during heat waves.

## Slide 11: Exploring Historical Heat Wave Grid Stress
https://doi.org/10.57931/2001010

## Slide 12: What About Future Heat Waves?
+5.9% in top-100 hourly loads due to climate change
Summer (Jun-Jul-Aug) load duration curves based on the 2019 weather year

## Slide 13: Exploring Future Heat Wave Grid Stress
https://doi.org/10.57931/2001010

## Slide 14: Simulating Multiple Weather Years to Explore Uncertainty
The prior example used a single weather year, but we can run many unique weather years through PNNL’s wind, load, and solar models:
  All years have the same total annual energy consumption by design
  Absolute magnitude and timing of peak demand varies significantly depending on the weather each year
2019 weather year

## Slide 15: Simulating Multiple Weather Years to Explore Uncertainty
Select weather years with extreme peaks for testing resilience…
Select weather years with late season peaks to assess reliability with low hydro…
The prior example used a single weather year, but we can run many unique weather years through PNNL’s wind, load, and solar models:
  All years have the same total annual energy consumption by design
  Absolute magnitude and timing of peak demand varies significantly depending on the weather each year

## Slide 16
At the seasonal time scale, there is often complementarity between wind and solar to address high load periods. For seasonal droughts, hydro, natural gas and transmission also need to be considered.
1980-2019
Summer high load,
low wind,
high solar
Winter
high load,
high wind,
low solar
Wind Solar and Load Cycles Vary Depending on the Region and Season

## Slide 17
Energy droughts help understand storage and regional transmission needs and whether market mechanisms incentivize those operations.
Bracken et al. ( in revision)
Coincident Datasets Help Identify Periods of Potential Stress

## Slide 18
Interannual variations in hydropower generation are expected and need to be considered in power system studies.
2018
July hydropower generation by power plant. Hydropower datasets include weekly potential generation and flexibility.
July 2015
Very high
Above normal
Normal
Below normal
Very low
July 2018
Hydropower Datasets Are Available for Input Into Power System Models

## Slide 19: Sharing Data and Models
godeeep.pnnl.gov
Open-source, vetted datasets are available in multiple formats in support of targeted questions by industry.

## Slide 20: Key Messages and Results
To assess the resilience and reliability of the bulk power system, it is critical to evaluate system performance with coincident load-wind-solar-hydro conditions and across a wide range of historical and projected weather conditions.
We are translating scientific understanding into actionable power-system relevant data and insights for use in long-term planning.
The conditions that stressed your system in the past may not be the ones that stress your system in the future.
Innovations:
  Spatially- and temporally-coincident load, wind, and solar data
  Capture consistent and realistic impacts on electricity supply and demand for use in stress testing projected infrastructure
  Quantitative characterization of wind and solar droughts

## Slide 21: Datasets, Models, and Funding
Key Datasets
Climate Forcing
  Jones, A. D., Rastogi, D., Vahmani, P., Stansfield, A., Reed, K., Thurber, T., Ullrich, P., & Rice, J. S. (2022). IM3/HyperFACETS Thermodynamic Global Warming (TGW) Simulation Datasets (v1.0.0) [Data set]. MSD-LIVE Data Repository. https://doi.org/10.57931/1885756
Wind and Solar Generation
  Bracken, C., Thurber, T., & Voisin, N. (2023). Hourly Wind and Solar Generation Profiles at 1/8th Degree Resolution (v1.0.0) [Data set]. Zenodo. https://doi.org/10.5281/zenodo.10214348
Key Models
Capacity Expansion Regional Feasibility (CERF): https://immm-sfa.github.io/cerf/
Grid Operations (GO): https://immm-sfa.github.io/go/
Renewable Energy Potential (reV): https://nrel.github.io/reV/
Total ELectricity Loads (TELL): https://immm-sfa.github.io/tell/
Funding
Various elements of this research were independently funded by DOE BER, DOE WPTO, and internal funding from PNNL